Sep 23, 2025
Kernel Recipes’25, Paris
Overcoming Observer Effects in Memory Management with DAMON
SeongJae Park (SJ) <sj@kernel.org> <sjpark@meta.com>
QR code
generated from https://qr.io
https://damonitor.github.io

---
Table of Contents
- Observer Effects in Memory Management – 5 mins
- How DAMON Overcomes the Observer Effect – 20 mins
- DAMON Use Cases – 5 mins
- Getting Started – 2 mins
- QnA – 8 mins

---
Observer Effects in
Memory Management

---
Memory Management for Better Data Placement
- Goal: process more data
- Limitation: fast memory devices are expensive (640 KB is not enough)
- H/W solution: memory devices of different speed/cost (cache, DRAM, CXL, SSD, …)
- S/W solution: access-aware data placement
  - Reclaim cold data by writeback on swap device or storage
  - Migrate hot data to faster NUMA nodes
  - Use huge pages for hot data
  - But, how it knows the access pattern?

---
Data Accesses: Microscope Events on Space/Time of Memory
Time
Address

---
Data Access Monitoring for MM: Ideal, Real and DAMON
- Ideal: precise (every bit), complete (every moment), light (prod online)
- Real: Expensive (observer effects), You Ain’t Gonna Need It
  - Observer effect is inevitable: Add monitoring-purpose memory access for each memory access
  - Even quantum physics PhD can live without knowing where each electron is at the moment
- Linux: Adopt non-ideal but practical mechanisms
  - Pseudo-LRU for finding cold data (reclaim)
  - Page fault-based throttled monitoring for hot data (NUMA blancing)
  - DAMON: a subsystem for practical access monitoring based holistic memory managements

---
How DAMON Handles
The Observer Effects:
Region-based Sampling

---
Region: Access Monitoring Unit for DAMON
- Defined as the reasonably-atomic unit of data access
  - A sub-area of the memory’s space-time
  - A collection of adjacent elements that having similar access pattern
- By the definition, access check of one element per region is enough
- e.g., “This page is accessed within last 1 second; a cacheline is checked”
$ cat wonder_region_1
We’re all mad [un]accessed here

---
Fixed Space/Time Granularity, Boolean Access Frequency
- Time overhead: “memory size / space granularity”
- Space overhead: “time overhead * monitoring time / time granularity”
- Overhead is reducible and controllable
- Ruled by memory size and monitoring time, finding best granularity is challenging
Time
We’re all mad accessed here
Region
We’re all mad unaccessed here
Sampling interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate (sampled) access check results via per-region counter
Now
Time
1
0
0
1
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate (sampled) access check results via per-region counter
Now
Time
1	2
0	1
0	0
1	2
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate (sampled) access check results via per-region counter
Now
Time
1	2	3
0	1	1
0	0	1
1	2	2
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate (sampled) access check results via per-region counter
Now
Time
1	2	3	0
0	1	1	0
0	0	1	0
1	2	2	0
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate (sampled) access check results via per-region counter
Now
Time
1	2	3	0 1	2	3
0	1	1	0 1	1	1
0	0	1	0 0	0	0
1	2	2	0 1	2	3
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate (sampled) access check results via per-region counter
Now
Time
1	2	3	0 1	2	3	0 1	2	2
0	1	1	0 1	1	1	0 1	1	2
0	0	1	0 0	0	0	0 1	1	1
1	2	2	0 1	2	3	0 1	1	2
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
- Accumulate access checks via per-region counter
- Reduce space overhead to “1/N”
- Still, O(memory size * total monitoring time)
Time
3	3	2
1	1	2
1	0	1
2	3	2
Region
Aggregate interval
Address

---
How DAMON Handles
The Observer Effects:
Auto-Tuned Space Control

---
Problems of Fixed Space Granularity
- Adjacent regions of similar hotness are wastes
- Restrict fine-grained space monitoring
Time
3	3	2
1	1	2
1	0	1
2	3	2
Region
Aggregate interval
Address

---
Auto-tuned Dynamic Space Granularity: Mechanisms (1/2)
- Repeat merging the wasteful regions and randomly splitting regions
  - The number of region == number of different access patterns
- Let user set min/max number of total regions
Time
3	3	2
1	1
	0	1
2	3	2
Region
Aggregate interval
Address

---
Auto-tuned Dynamic Space Granularity: Mechanisms (2/2)
- Repeat merging the wasteful regions and randomly splitting regions
  - The number of region == number of different access patterns
- Let user set min/max number of regions
Time
3	3	2
1	1
	0	1
2	3	2
Region
Aggregate interval
Address

---
Auto-tuned Dynamic Space Granularity: Overhead/Accuracy
- Time overhead: min(different access patterns, max number of regions)
  - No more ruled by memory size, fully controlled and auto-tuned
- Accuracy: best-effort high
  - Auto-tuned dynamic granularity can find accesses to small memory area
Time
3	3	2
1	1
	0	1
2	3	2
Region
Aggregate interval
Address

---
How DAMON Handles
The Observer Effects:
Time Optimization

---
Problems of Fixed Time Granularity Regions (1/2)
The definition of regions is not only about space, but also about time
Time
Region
Aggregate interval
Address

---
Inefficiency of Fixed Time Granularity Regions (2/2)
- The definition of regions is not only about space, but also about time
- Multiple time-adjacent regions of similar hotness: only waste
Time
Region
Aggregate interval
Address

---
Dynamic Time Granularity (1/3)
- Count how long the hotness has kept
- Snapshot contains history of useful length
Now
Time
1
1
1
1
Region
Aggregate interval
Address

---
Dynamic Time Granularity (2/3)
- Count how long the hotness has kept
- Snapshot contains history of useful length
This snapshot can be discarded
Now
Time
1	2
1	2
1	1
1	1
Region
Aggregate interval
Address

---
Dynamic Time Granularity (3/3)
- Count how long the hotness has kept
- Snapshot contains history of useful length
This snapshot can be discarded
This snapshot can be discarded
Now
Time
1	2	1
1	2	3
1	1	1
1	1	1
Region
Aggregate interval
Address

---
Snapshot: The Output of DAMON
- O(max_nr_regions) time/space overhead
- Both time/space overheads are not ruled by memory size/monitoring time

---
How DAMON Handles
The Observer Effects:
Monitoring Intervals Auto-tuning

---
FAQ: DAMON output looks only cold, only hot, or just random
- Frequent Answer: Have you tuned the monitoring intervals?
  - IOW, the default intervals (5ms sampling, 100ms aggregation) are not really suggested ones

---
If Intervals Are Appropriate: Meaningful Hot/Cold Regions
Meaningful enough to make some memory management decisions
Time
1	2	3	1	2	3	1	2	2
0	1	1	1	1	1	1	1	2
0	0	1	0	0	0	1	1	1
1	2	2	1	2	3	1	1	2
Region
Aggregation interval
Sampling interval
Address

---
If Intervals Are Too Short: Everything Looks Cold
Time
1	1	1	0	1	1	0	1	1
0	0	0	0	0	0	0	0	0
0	0	0	0	0	0	0	0	0
1	1	1	0	0	0	0	0	0
Region
Aggregation interval
Sampling interval
Address

---
If Intervals Are Too Long: Everything Looks Hot
1	2	3	1	2	3	1	2	3
1	2	3	1	2	3	1	2	3
1	2	3	1	1	2	1	2	3
1	2	3	1	2	3	1	2	3
Region
Aggregation interval
Sampling interval
Address

---
If Sampling:Aggregation Interval ratio is Too Low: Meaningless Samples
- Most sampling returns “negative”: unnecessary CPU cycle waste
- On large systems, sampling quality can also degrade
  - Not enough time for workloads to leave footprints
Region
Aggregation interval
Sampling interval
Address

---
Intervals Tuning Guideline
- If it looks too cold, increase intervals
- If it loos too hot, decrease intervals
- Change both sampling and aggregation intervals in same ratio
- Repeat until meaningful snapshot is made
- Time consuming and repetitive for different workloads
- Guideline was added more than 3.5 years after DAMON be merged upstream!
- Could be automated?

---
Aimed Monitoring Output-oriented Intervals Auto-tuning
- Change Question: How to do? (mechanism) → What to achieve? (final goal, policy)
- Let users specify
  - Desired amount of access events to capture in each snapshot
  - Minimum and maximum sampling intervals
- Find proper sampling/aggregation intervals for the desire using feedback loop
  - If less than desired events are captured in current snapshot, increase intervals
  - If more than desired events are captured in current snapshot, decrease intervals
  - Min/max sampling intervals ensure auto-tune goes no too long
- Available on mainline from v6.15

---
Monitoring Intervals Auto-tuning Parameters
- Parameters for parameters auto-tuning, but easy to set
- Suggestion
  - Desired access events per snapshot: 4% of maximum events that can be captured in snapshot
    - Applies Pareto principle (80:20 rule) twice, assume to capture 80% * 80% = 64% real access
  - Min/max sampling intervals: 5ms and 10s
  - Sampling:aggregation intervals ratio: 1:20
    - Only a few different actions are required, 20 is high enough

---
Intervals Auto-tuning on a Real-world Server Workload
- Sampling interval and tuning score continuously change, and converge for given situation
  - Sampling interval converges to 370ms under usual load, ~4-5 seconds under light load
  - Tuning score converges to the goal (10,000 bp)

---
Intervals Auto-Tuning on Real World Server Workloads
- Meaningful access patterns found on three different workloads including 1 TiB memory size workload
- 0.0% CPU time consumed for the monitoring

---
How DAMON Handles
The Observer Effects:
Access-aware
Memory Management

---
Utilizing DAMON for Access-aware Memory Management
- Profiling (e.g., GIF demo link)
  - For finding rooms to improve, e.g., capacity planning
- Profiling-guided Optimizations
  - Could be done on both offline and online
- Why not let kernel just (transparently) works?

---
Utilizing DAMON for Access-aware Memory Management
- Profiling (e.g., GIF demo link)
  - For finding rooms to improve, e.g., capacity planning
- Profiling-guided Optimizations
  - Could be done on both offline and online
- Why not let kernel just (transparently) works?

---
Utilizing DAMON for Access-aware Memory Management
- Profiling (e.g., GIF demo link)
  - For finding rooms to improve, e.g., capacity planning
- Profiling-guided Optimizations
  - Could be done on both offline and online
- Why not let kernel just (transparently) works?

---
DAMOS: Data Access Monitoring-based Operation Schemes
- The other face of DAMON
- Let users define schemes
  - Memory operation actions to apply to regions of specific access pattern
- Once per user-defined time interval
  - find the regions of the condition from the snapshot and apply the action
- Finding optimum “access pattern” on dynamic environments is challenging
  - Uncontrolled DAMOS could byte you!
# # pageout memory regions that not accessed for >=5 seconds
# damo start --damos_action pageout --damos_access_rate 0% 0% --damos_age 5s max

---
Use Cases

---
Proactive Cold Memory Reclamation
- Proactively find cold pages and reclaim
- Reduce memory footprint without performance degradation
- Reduce memory pressure occurrences and help (automated) capacity planning
- AWS Aurora Serverless v2 uses this for memory auto-scaling

---
Memory Tiering
- Migrate hot data in slow NUMA node to fast NUMA node, cold data in opposite direction
  - e.g., CXL and DRAM nodes
- SK Hynix developed and utilizing this for their Heterogeneous Memory SDK
- Meta’s improved self-tuning version shows ~7.34% performance improvement on a test workload (Taobench)
- Cgroup fairness-aware extension is also available in RFC

---
Access-aware Dynamic Memory Interleaving
- Memory interleaving: interleave placement on allocation time for bandwidth control
- Dynamically interleave (migrate) data for dynamic access pattern in access-aware order
- Micron developed for their internal project
- Micron’s test shows 25% performance improvement

---
Page Level Data Access Monitoring
- Different types of pages have different management mechanisms
- Breakdown data access pattern for specific types of pages
- Developed by Meta for hugepage and LRU-active pages access pattern profiling
Per-page type access pattern of a production workload

---
Fleet-wide Data Access Monitoring
- Transform DAMON snapshot into memory idle time distribution (percentiles)
- Can easily aggregated and intuitively visualized (idle time percentiles or cold memory tails)
- Developed by Meta for fleet-wide real workloads access pattern profiling
Cold memory tails (left) and idle memory time percentiles (right) of real workloads

---
Getting Started

---
Where to Get Started: https://damonitor.github.io
- Project website
- Contains getting started guides and all resources for users and developers
- Should have all you need to get started
  - If not, report it please

---
Availability
- Merged into the mainline from v5.15
- Backported and enabled on major Linux distro kernels
  - Major distros: Alma, Amazon, Android, Arch, CentOS, Debian, Fedora, Oracle, …
- DAMON user-space tool (damo) is available on major packaging systems
  - Arch, Debian, Fedora, PyPi, ...

---
Interfaces
- DAMON user-space tool: Recommended for general usages from user-space
- DAMON modules: Recommended for specific usages
- DAMON sysfs interface: Recommended for user-space program development
- Kernel API: Recommended for kernel programmers

---
Community: For Questions, Help, Patch Reviews
- Public mailing list (https://lore.kernel.org/damon)
- Bi-weekly virtual meetup
  - Occasional/regular private meetings on demand
- Not used to mail-based development? Try hkml
  - Developed and maintained for DAMON and Linux kernel developers
- The future of DAMON is open and up to you
  - “Prefer random evolution over intelligent design”

---
Summary: That’s DAMON
- DAMON is a Linux kernel subsystem
  - For practical access monitoring based holistic memory managements
- Companies, researchers and individuals are using it for better memory managements
- The future is open and up to the community
  - Make your selfish voice

---
Questions?
- You can also ask questions anytime to
  - sj@kernel.org
  - Public mailing list (https://lore.kernel.org/damon)
  - Bi-weekly virtual meetup
  - Occasional/regular private meetings on demand
  - Project website (https://damonitor.github.io)

---
Backup Slides

---
DAMON_STAT: Recommended Way For System-wide Access Monitoring
- Kernel module running DAMON for the entire physical address space
- Use intervals auto-tuning with the suggested auto-tune parameters
- Extract Idle time percentile
  - distribution of per-byte memory idle times (time the byte was not accessed)
  - P75 idle time 2minutes: 75 percent of the memory was accessed at least once in last 2 minutes; rest 25 percent of memory was not accessed at all for last 2 minutes
- Extract estimated memory bandwidth
  - Memory bandwidth estimated based on access events that captured in the last snapshot
- Recommended way for system-wide access monitoring
  - Easy to enable (CONFIG_DAMON_STAT_DEFAULT_ENABLED=y), aggregate, compare
  - Can be enabled/disabled at build, boot time and runtime

---
Idle Time Percentiles
- Idle time: How long the region kept being not accessed (access frequency 0)
- Idle time percentiles: Percentiles of sorted per-byte idle times
Unsorted snapshot

---
Idle Time Percentiles
- Idle time: How long the region kept being not accessed (access frequency 0)
- Idle time percentiles: Percentiles of sorted per-byte idle times
Unsorted snapshot
Sorted by access frequency

---
Idle Time Percentiles
- Idle time: How long the region kept being not accessed (access frequency 0)
- Idle time percentiles: Percentiles of sorted per-byte idle times
Unsorted snapshot
Sorted by access frequency
P50 idle time

---
Idle Time Percentiles
- Idle time: How long the region kept being not accessed (access frequency 0)
- Idle time percentiles: Percentiles of sorted per-byte idle times
Unsorted snapshot
Sorted by access frequency
P50 idle time
P75 idle time

---
Idle Time Percentiles
- Idle time: How long the region kept being not accessed (access frequency 0)
- Idle time percentiles: Percentiles of sorted per-byte idle times
Unsorted snapshot
Sorted by access frequency
P50 idle time
P75 idle time
P99 idle time

---
DAMON_STAT: Recommended Way For System-wide Access Monitoring
- Kernel module running DAMON for the entire physical address space
- Use intervals auto-tuning with the suggested auto-tune parameters
- Extract Idle time percentile
  - distribution of per-byte memory idle times (time the byte was not accessed)
  - P75 idle time 2minutes: 75 percent of the memory was accessed at least once in last 2 minutes; rest 25 percent of memory was not accessed at all for last 2 minutes
- Extract estimated memory bandwidth
  - Memory bandwidth estimated based on access events that captured in the last snapshot
- Recommended way for system-wide access monitoring
  - Easy to enable (CONFIG_DAMON_STAT_DEFAULT_ENABLED=y), aggregate, compare
  - Can be enabled/disabled at build, boot time and runtime

---
Results on a Real Workload: Auto-tuned Total Memory Idle Time Percentiles
Small hot memory, exponentially increasing idle time (long tail of cold pages)

---
Results on a Real Workload: Active vs Inactive Pages Idle Time Breakdown
Active pages have rooms to be more hot than inactive
(ideally, p100 of active should < p0 of inactive)

---
Results on a Real Workload: Per Page Type Idle Time Breakdown
You can check if your workload has expected access pattern

---
DAMOS Filter: Fine-Control Access-aware System Operation Targets
- Define target memory with non-access-pattern information
  - Page level filters: anon, owned cgroup, hugepage, LRU-activeness
  - Non-page level filters: address
  - “pageout cold pages of NUMA node 1 that associated with cgroup A and file-backed”
  - Can be useful for fine-grained monitoring, too
    - (“stat”, instead of “pageout”)

---
DAMOS Quota: Control Access-aware System Operation Aggressiveness
- Six fixed thresholds (min/max size, access frequency, age) are unnecessary in many cases
- Setting thresholds flexibly and controlling aggressiveness works in many cases
  - Single control knob
- Quota set the aggressiveness limit as amount of memory to apply action per a time interval
- Access pattern based prioritization is applied under the quota
- “pageout cold pages up to 100 MiB per second using <2% CPU time, coldest ones first”

---
Quota Auto-tuning: Auto-tuned Access-aware System Operations
- Quota tuning is manual and repetitive
- Change the question for user: How to do (mechanism) → What to achieve (final goal)
- Let users specify goal of the quota as a value of a metrics
  - Metrics: PSI level, NUMA node memory utilization, workload’s latency, bandwidth, TPS, …
  - e.g., “reclaim cold pages aiming 0.5% memory PSI”
- DAMOS adjusts quota using feedback loop, for current value of the metric
  - e.g., If memory PSI is 0.1% increase quota for reclaiming cold pages (reclaim more warm pages)

---
Controlled and Auto-tuned Access-aware System Operation Performance
- Parsec3/splash2x.fft
- Page out regions that not accessed for >=5 seconds, up to 1GiB/sec, using up to 100ms/sec, aiming 10ms/sec memory pressure stall
	Runtime	RSS
Baseline	50.489s	10.005 GiB
+DAMOS-reclaim	120s	4.955 GiB
+Quota	51.772s	8.527 GiB
+Goal	49.741s	9.721 GiB

---
Real-world DAMON Use Cases:
Proactive Reclamation and
CXL Memory Tiering

---
Proactive Reclamation
- Reactive reclamation: Reclaim cold memory when memory pressure happens
- Proactively reclamation: Reclaim cold memory before memory pressure
- Benefit 1: Reduce memory footprint without performance degradation
- Benefit 2: Minimize degradation from direct reclamation
- Known usages: Google, Meta, and Amazon
  - Each company uses its own implementation for its usage
- AWS uses DAMOS-based implementation since 2022

---
CXL Memory Tiering
- CXL-tiered memory: Put CXL memory between DRAM and NVM
  - Pros: Higher capacity with lower price (higher efficiency)
- Challenge: Dynamic placement of pages (CXL mem is slower than DRAM)
- DAMON-based approach: Place hot pages on DRAM node, Place cold pages on CXL node
- SK hynix developed their CXL memory SDK (HMSDK) using DAMOS
  - Reports ~12.9% speed up

---
Architectures

---
Execution Model: Kernel Thread per Requests
- “struct damon_ctx”: Data structure for DAMON user input/output containing
  - User requests: target address space, address range, intervals, DAMOS schemes
  - Operation results: access snapshot, DAMOS stats
- “kdamond”: DAMON worker thread
  - Create one kdamond per “damon_ctx”
    - In future, could support multiple “damon_ctx” per kdamond
    - In future, could separate DAMOS to another thread (maybe useful for cgroup charging)
  - Allows async DAMON execution and multiple kdamonds (CPUs) scaling

---
Extensible Layers
User-space
Tools
DAMO
datop
General-purpose User ABI
Special-purpose Modules
DAMON API User
Kernel Modules
DAMON_SYSFS
DAMON_DBGFS
DAMON_RECLAIM
DAMON_LRU_SORT
DAMON_WSS
DAMON Application Programming Interface
DAMON
DAMOS
Adaptive Regions Adjustment
Action and Pattern
Core Logic
Region-based Sampling
Quotas and Prioritization
Access Frequency Monitoring
Feedback-based auto-tuning
Advanced Regions Adjustment
Watermarks
Parameters Auto-tuning
Filters
DAMON Operations Set Registration Interface
Operations Set
paddr
vaddr
Read/write-only
NUMA-cpus-only
Primitives
that DAMON
depends on
PTE/VMA/rmap, ...
AMD IBS
LRU State

---
Extensible Layers
User-space
Tools
DAMO
datop
General-purpose User ABI
Special-purpose Modules
DAMON API User
Kernel Modules
DAMON_SYSFS
DAMON_DBGFS
DAMON_RECLAIM
DAMON_LRU_SORT
DAMON_WSS
DAMON Application Programming Interface
DAMON
DAMOS
Adaptive Regions Adjustment
Action and Pattern
Core Logic
Region-based Sampling
Quotas and Prioritization
Access Frequency Monitoring
Feedback-based auto-tuning
Advanced Regions Adjustment
Watermarks
Parameters Auto-tuning
Filters
DAMON Operations Set Registration Interface
Operations Set
paddr
vaddr
Read/write-only
NUMA-cpus-only
Primitives
that DAMON
depends on
PTE/VMA/rmap, ...
AMD IBS
LRU State

---
Extensible Layers
User-space
Tools
DAMO
datop
General-purpose User ABI
Special-purpose Modules
DAMON API User
Kernel Modules
DAMON_SYSFS
DAMON_DBGFS
DAMON_RECLAIM
DAMON_LRU_SORT
DAMON_WSS
DAMON Application Programming Interface
DAMON
DAMOS
Adaptive Regions Adjustment
Action and Pattern
Core Logic
Region-based Sampling
Quotas and Prioritization
Access Frequency Monitoring
Feedback-based auto-tuning
Advanced Regions Adjustment
Watermarks
Parameters Auto-tuning
Filters
DAMON Operations Set Registration Interface
Operations Set
paddr
vaddr
Read/write-only
NUMA-cpus-only
Primitives
that DAMON
depends on
PTE/VMA/rmap, ...
AMD IBS
LRU State

---
DAMOS Quotas: Intuitive Aggressiveness Control
- Before applying DAMOS schemes
  - Set temperature-based priority score of each region
  - Build “priority score”: “total size of regions of the priority” histogram
  - Find lowest priority threshold for the scheme meeting the quota
  - Skip applying action to regions having lower-than-threshold priority scores
- Single snapshot and histogram iteration: O(<=user-defined-N)
- Quota auto-tuning: A simple proportional feedback algorithm
  - Reward metrics: Arbitrary user-input or self-retrievable metrics like memory PSI

---
DAMOS Filters: Fine-grained Target Selection
- Before applying DAMOS action, check the properties of region and skip action if needed
- Non-page granular (high level) filters
  - Filtered out before applying actions
  - Address ranges (e.g., NUMA nodes or Zone)
  - DAMON-defined monitoring target (e.g., process)
- Page granular (low level) filters
  - Filtered out in the middle of actions in page level
  - Anon/File-backed
  - Belonging memory cgroup
  - page_idle()

---
Pseudo-code of DAMON v5.15
While True:
for region in regions:
if region.accessed():
region.nr_accesses += 1
sleep(sampling_interval)
if now() % aggregation_interval:
merge(regions)
user_callback(regions)
for region in regions:
region.nr_accesses = 0
split(regions)

---
DAMON accuracy on Low-locality Space/Workloads
- It is proven to work on real world products for years
- Pareto principle and unconcious bias will make the pattern
  - Entropy-full situation is when the data center is doom-ed
- “age” avoid immature decision
- More works for accuracy improvement will be continued
- DAMON could be decoupled with the region-based mechanisms in future
- Let’s collect data and continue discussions together

---
Can DAMON Extended for Non-snapshot Access Patterns?
- TL; DR: Yes, why not?
- DAMON is for any access information; Snapshot is one of the representations
- If the information/representation is useful for users, DAMON can add support
- We started discussion for Memory bandwidth visibility

---
Can DAMON Use features Other than PTE Accessed bits?
- The extensible layer allows it
- AMD IBS and page fault-based appaoraches (e.g., PTE_NONE) are on the table
- In future, if GPU provides access check feature, we can extend to use it
- Such extension would allow
  - More lightweight and precise monitoring
  - Access source, read/write-aware monitroing
  - Kernel memory access monitoring

---
DAMOS for Efficient and Fine-grained Data Access Monitoring
- DAMOS_STAT
  - Special action making no system change but expose the scheme-internal information
  - Let user knows which of the memory are eligible for the scheme
- With DAMOS filters, can do page level properties-based monitoring
  - “How much of >2 minutes unaccessed memory are in hugepages and belong to cgroup A?”
- With DAMOS quotas, can do overhead-controlled monitoring