Feb 2, 2025
FOSDEM’25, Brussels
DAMON: Kernel Subsystem for Data Access Monitoring and Access-aware System Operations
SeongJae Park (SJ) <sj@kernel.org> <sjpark@meta.com>
QR code
generated from https://qr.io
https://damonitor.github.io

---
DAMON: Kernel Subsystem for Data Access Monitoring and Access-aware System Operations

---
Data Accesses: Events on Space/Time of Memory
Time
Address

---
Data Access Monitoring: Hope, Real, and DAMON
- Hope: Precise, Complete, Light
  - Time granularity: CPU cycle / # CPUs (or, speed of light)
  - Space granularity: bit (or, electron)
  - Keep complete history (from Bigbang)
  - Lightweight enough to run on production systems
- Real: Expensive, YAGNI without tradeoff
  - O(memory size) time, O(memory size * total monitoring time) space overhead
  - Do you really care if a bit was accessed five years ago?
- DAMON: accuracy vs overhead tradeoff
  - Scalable, best-effort, aim real-world products usage

---
Region-based Space Handling

---
Region: Access Monitoring Unit
- Defined as
  - A sub-area of the memory’s space-time
  - A collection of adjacent elements that having similar access pattern
- Access check of one element per region is enough
- e.g., “This page is accessed within last 1 second; a cacheline is checked”
$ cat wonder_region_1
We’re all mad [un]accessed here

---
Fixed Space/Time Granularity, <=1 Access Frequency
- Sort of periodic fixed granularity idleness monitoring
- Time overhead: “memory size / space granularity”
- Space overhead: “time overhead * monitoring time / time granularity”
- Reduced, but still ruled by memory size and total monitoring time
Time
We’re all mad accessed here
Region
We’re all mad unaccessed here
Sampling interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate access checks via per-region counter
Now
Time
1
0
0
1
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate access checks via per-region counter
Now
Time
1	2
0	1
0	0
1	2
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate access checks via per-region counter
Now
Time
1	2	3
0	1	1
0	0	1
1	2	2
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate access checks via per-region counter
Now
Time
1	2	3	0
0	1	1	0
0	0	1	0
1	2	2	0
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate access checks via per-region counter
Now
Time
1	2	3	0 1	2	3
0	1	1	0 1	1	1
0	0	1	0 0	0	0
1	2	2	0 1	2	3
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
Accumulate access checks via per-region counter
Now
Time
1	2	3	0 1	2	3	0 1	2	2
0	1	1	0 1	1	1	0 1	1	2
0	0	1	0 0	0	0	0 1	1	1
1	2	2	0 1	2	3	0 1	1	2
Region
Sampling interval
Aggregate interval
Address

---
Fixed Space/Time Granularity, <=N Access Frequency
- Accumulate access checks via per-region counter
- Reduce space overhead to “1/N”
- Still, O(memory size * total monitoring time)
Time
3	3	2
1	1	2
1	0	1
2	3	2
Region
Aggregate interval
Address

---
Inefficiency of Fixed Space Granularity
Adjacent regions of similar hotness
Time
3	3	2
1	1	2
1	0	1
2	3	2
Region
Aggregate interval
Address

---
Dynamic Space Granularity: Mechanisms
- Repeat merging the wasteful regions and randomly splitting regions
  - The number of region == number of different access patterns
- Let user set min/max number of total regions
Time
3	3	2
1	1
	0	1
2	3	2
Region
Aggregate interval
Address

---
Dynamic Space Granularity: Mechanisms
- Merge the wasteful regions and randomly split region
  - The number of region == number of different access patterns
- Let user set min/max number of regions
Time
3	3	2
1	1
	0	1
2	3	2
Region
Aggregate interval
Address

---
Dynamic Space Granularity: Overhead/Accuracy
- Time overhead: min(different access patterns, max number of regions)
  - No more ruled by arbitrary memory size
- Accuracy: best-effort high
  - Lower-bound accuracy can be set via min_nr_regions
Time
3	3	2
1	1
	0	1
2	3	2
Region
Aggregate interval
Address

---
Age Counting for History Handling

---
Inefficiency of Fixed Time Granularity Regions (1/2)
The definition of regions is not only about space, but also about time
Time
Region
Aggregate interval
Address

---
Inefficiency of Fixed Time Granularity Regions (2/2)
- The definition of regions is not only about space, but also about time
- Multiple time-adjacent regions of similar hotness: only waste
Time
Region
Aggregate interval
Address

---
Dynamic Time Granularity (1/3)
- Count how long the hotness has kept
- Snapshot contains history of useful length
Now
Time
1
1
1
1
Region
Aggregate interval
Address

---
Dynamic Time Granularity (2/3)
- Count how long the hotness has kept
- Snapshot contains history of useful length
This snapshot can be discarded
Now
Time
1	2
1	2
1	1
1	1
Region
Aggregate interval
Address

---
Dynamic Time Granularity (3/3)
- Count how long the hotness has kept
- Snapshot contains history of useful length
This snapshot can be discarded
This snapshot can be discarded
Now
Time
1	2	1
1	2	3
1	1	1
1	1	1
Region
Aggregate interval
Address

---
Snapshot: The Output of DAMON
- O(max_nr_regions) time/space overhead
- Both time/space overheads are not ruled by memory size/monitoring time

---
How Accurate, How Heavy?
- Up to you: Under the control, best effort (highest accuracy, lowest overhead)
- Being successfully used on real world products for years
- 3-4% single CPU usage is commonly reported from real world products
  - Many rooms to improve: the goal is turning it on by default everywhere

---
Potential, or Aimed Usages
- Profiling (e.g., GIF demo link)
  - Help better understand and find rooms for improvements
- Profiling-guided Optimizations
  - Could be done on both offline and online
- Why not let kernel just (transparently) works?

---
Potential, or Aimed Usages
- Profiling (e.g., GIF demo link)
  - Help better understand and find rooms for improvements
- Profiling-guided Optimizations
  - Could be done on both offline and online
- Why not let kernel just (transparently) works?

---
Potential, or Aimed Usages
- Profiling (e.g., GIF demo link)
  - Help better understand and find rooms for improvements
- Profiling-guided Optimizations
  - Could be done on both offline and online
- Why not let kernel just (transparently) works?

---
DAMON: Kernel Subsystem for Data Access Monitoring and Access-aware System Operations

---
DAMOS: Data Access Monitoring-based Operation Schemes
- Another side of DAMON
- Let users define schemes
  - Memory operation actions to apply to regions of specific access pattern
- Once per user-defined time interval
  - find the regions of the condition from the snapshot and apply the action
- Additional features for production level control are provided
  - Finding optimum “access pattern” on dynamic environments is challenging
# # pageout memory regions that not accessed for >=5 seconds
# damo start --damos_action pageout --damos_access_rate 0% 0% --damos_age 5s max

---
Features for Production Quality DAMOS Control
- Filters: define target memory with non-access-pattern information
  - “pageout cold pages of NUMA node 1 that associated with cgroup A and file-backed”
- Quota: set aggressiveness of DAMOS
  - Access pattern based prioritization is applied under the quota
  - “pageout cold pages up to 100 MiB per second using <2% CPU time, coldest ones first”
- Quota auto-tuning: auto-tune quota for user-defined target metric
  - “pageout cold pages aiming 0.05% of memory pressure (coldest ones first)”

---
DAMOS for Efficient and Fine-grained Data Access Monitoring
- DAMOS_STAT
  - Special action making no system change but expose the scheme-internal information
  - Let user knows which of the memory are eligible for the scheme
- With DAMOS filters, can do page level properties-based monitoring
  - “How much of >2 minutes unaccessed memory are in hugepages and belong to cgroup A?”
- With DAMOS quotas, can do overhead-controlled monitoring

---
Getting Started

---
Availability
- Merged into the mainline from v5.15
- Backported and enabled on major Linux distro kernels
  - Major distros: Amazon, Android, Arch, Debian, Fedora, Oracle, …
- DAMON user-space tool (damo) is available on major packaging systems
  - Arch, Debian, Fedora, PyPi, ...

---
How can I Use DAMON?
- Kernel API: Recommended for kernel programmers
- DAMON sysfs interface: Recommended for user-space program development
- DAMON user-space tool: Recommended for general usages from user-space
- DAMON modules: Recommended for specific usages
- If you don’t know what to do first, DAMON tests suite

---
Community: For Questions, Help, Patch Reviews
- Public mailing list (https://lore.kernel.org/damon)
- Bi-weekly virtual meetup
  - Occasional/regular private meetings on demand
- Project website (https://damonitor.github.io)
  - Starting point for DAMON users and developers
- The future of DAMON is open and up to you
  - “Prefer random evolution over intelligent design”

---
Summary: That’s DAMON
- DAMON is a kernel subsystem
  - For data access monitoring and access-aware system operations
- The future is open and up to the community
  - Make your selfish voice

---
Questions?
- You can also ask questions anytime to
  - sj@kernel.org
  - Public mailing list (https://lore.kernel.org/damon)
  - Bi-weekly virtual meetup
  - Occasional/regular private meetings on demand
  - Project website (https://damonitor.github.io)
- These slides are also available at
  - https://github.com/damonitor/talks/blob/master/2025/fosdem/damon_fosdem25.pdf

---
Backup Slides

---
Real-world DAMON Use Cases:
Proactive Reclamation and
CXL Memory Tiering

---
Proactive Reclamation
- Reactive reclamation: Reclaim cold memory when memory pressure happens
- Proactively reclamation: Reclaim cold memory before memory pressure
- Benefit 1: Reduce memory footprint without performance degradation
- Benefit 2: Minimize degradation from direct reclamation
- Known usages: Google, Meta, and Amazon
  - Each company uses its own implementation for its usage
- AWS uses DAMOS-based implementation since 2022

---
CXL Memory Tiering
- CXL-tiered memory: Put CXL memory between DRAM and NVM
  - Pros: Higher capacity with lower price (higher efficiency)
- Challenge: Dynamic placement of pages (CXL mem is slower than DRAM)
- DAMON-based approach: Place hot pages on DRAM node, Place cold pages on CXL node
- SK hynix developed their CXL memory SDK (HMSDK) using DAMOS
  - Reports ~12.9% speed up

---
Architectures

---
Execution Model: Kernel Thread per Requests
- “struct damon_ctx”: Data structure for DAMON user input/output containing
  - User requests: target address space, address range, intervals, DAMOS schemes
  - Operation results: access snapshot, DAMOS stats
- “kdamond”: DAMON worker thread
  - Create one kdamond per “damon_ctx”
    - In future, could support multiple “damon_ctx” per kdamond
    - In future, could separate DAMOS to another thread (maybe useful for cgroup charging)
  - Allows async DAMON execution and multiple kdamonds (CPUs) scaling

---
Extensible Layers
User-space
Tools
DAMO
datop
General-purpose User ABI
Special-purpose Modules
DAMON API User
Kernel Modules
DAMON_SYSFS
DAMON_DBGFS
DAMON_RECLAIM
DAMON_LRU_SORT
DAMON_WSS
DAMON Application Programming Interface
DAMON
DAMOS
Adaptive Regions Adjustment
Action and Pattern
Core Logic
Region-based Sampling
Quotas and Prioritization
Access Frequency Monitoring
Feedback-based auto-tuning
Advanced Regions Adjustment
Watermarks
Parameters Auto-tuning
Filters
DAMON Operations Set Registration Interface
Operations Set
paddr
vaddr
Read/write-only
NUMA-cpus-only
Primitives
that DAMON
depends on
PTE/VMA/rmap, ...
AMD IBS
LRU State

---
Extensible Layers
User-space
Tools
DAMO
datop
General-purpose User ABI
Special-purpose Modules
DAMON API User
Kernel Modules
DAMON_SYSFS
DAMON_DBGFS
DAMON_RECLAIM
DAMON_LRU_SORT
DAMON_WSS
DAMON Application Programming Interface
DAMON
DAMOS
Adaptive Regions Adjustment
Action and Pattern
Core Logic
Region-based Sampling
Quotas and Prioritization
Access Frequency Monitoring
Feedback-based auto-tuning
Advanced Regions Adjustment
Watermarks
Parameters Auto-tuning
Filters
DAMON Operations Set Registration Interface
Operations Set
paddr
vaddr
Read/write-only
NUMA-cpus-only
Primitives
that DAMON
depends on
PTE/VMA/rmap, ...
AMD IBS
LRU State

---
Extensible Layers
User-space
Tools
DAMO
datop
General-purpose User ABI
Special-purpose Modules
DAMON API User
Kernel Modules
DAMON_SYSFS
DAMON_DBGFS
DAMON_RECLAIM
DAMON_LRU_SORT
DAMON_WSS
DAMON Application Programming Interface
DAMON
DAMOS
Adaptive Regions Adjustment
Action and Pattern
Core Logic
Region-based Sampling
Quotas and Prioritization
Access Frequency Monitoring
Feedback-based auto-tuning
Advanced Regions Adjustment
Watermarks
Parameters Auto-tuning
Filters
DAMON Operations Set Registration Interface
Operations Set
paddr
vaddr
Read/write-only
NUMA-cpus-only
Primitives
that DAMON
depends on
PTE/VMA/rmap, ...
AMD IBS
LRU State

---
DAMOS Quotas: Intuitive Aggressiveness Control
- Before applying DAMOS schemes
  - Set temperature-based priority score of each region
  - Build “priority score”: “total size of regions of the priority” histogram
  - Find lowest priority threshold for the scheme meeting the quota
  - Skip applying action to regions having lower-than-threshold priority scores
- Single snapshot and histogram iteration: O(<=user-defined-N)
- Quota auto-tuning: A simple proportional feedback algorithm
  - Reward metrics: Arbitrary user-input or self-retrievable metrics like memory PSI

---
DAMOS Filters: Fine-grained Target Selection
- Before applying DAMOS action, check the properties of region and skip action if needed
- Non-page granular (high level) filters
  - Filtered out before applying actions
  - Address ranges (e.g., NUMA nodes or Zone)
  - DAMON-defined monitoring target (e.g., process)
- Page granular (low level) filters
  - Filtered out in the middle of actions in page level
  - Anon/File-backed
  - Belonging memory cgroup
  - page_idle()

---
Pseudo-code of DAMON v5.15
While True:
for region in regions:
if region.accessed():
region.nr_accesses += 1
sleep(sampling_interval)
if now() % aggregation_interval:
merge(regions)
user_callback(regions)
for region in regions:
region.nr_accesses = 0
split(regions)

---
DAMON accuracy on Low-locality Space/Workloads
- It is proven to work on real world products for years
- Pareto principle and unconcious bias will make the pattern
  - Entropy-full situation is when the data center is doom-ed
- “age” avoid immature decision
- More works for accuracy improvement will be continued
- DAMON could be decoupled with the region-based mechanisms in future
- Let’s collect data and continue discussions together

---
Can DAMON Extended for Non-snapshot Access Patterns?
- TL; DR: Yes, why not?
- DAMON is for any access information; Snapshot is one of the representations
- If the information/representation is useful for users, DAMON can add support
- We started discussion for Memory bandwidth visibility

---
Can DAMON Use features Other than PTE Accessed bits?
- The extensible layer allows it
- AMD IBS and page fault-based appaoraches (e.g., PTE_NONE) are on the table
- In future, if GPU provides access check feature, we can extend to use it
- Such extension would allow
  - More lightweight and precise monitoring
  - Access source, read/write-aware monitroing
  - Kernel memory access monitoring

---
DAMON Monitoring Auto-tuning
- Aggregation interval tuning is mandatory for real-world DAMON usages
- Auto-tuning for the user-desired amount of access samples is under development
- Auto-tuning of max_nr_regions for user-desired CPU usage is a TODO